## Slide 1: FLUKA Estimators and Scoring
45th Karpacz Winter School
Feb. 2-8, 2009
Notes: <number>

## Slide 2: FLUKA Scoring & Results - Estimators
It is often said that Monte Carlo (MC) is a “mathematical experiment” The MC equivalent of the result of a real experiment (i.e., of a measurement) is called an estimator.
Just as a real measurement, an estimator is obtained by sampling from a statistical distribution and has a statistical error (and in general also a systematic one).
There are often several different techniques to measure the same physical quantity: in the same way the same quantity can be calculated using different kinds of estimators.
FLUKA offers numerous different estimators, i.e., directly from the input file the users can request scoring the respective quantities they are interested in.
As the latter is implemented in a very complete way, users are strongly encouraged to preferably use the built-in estimators with respect to user-defined scoring
For additional requirements FLUKA user routines are provided
Notes: <number>

## Slide 3: Built-In and User Scoring
Several pre-defined estimators can be activated in FLUKA.
One usually refers to these estimators as “scoring” capabilities
Users have also the possibility to build their own scoring through user routines, HOWEVER:
  Built-in scoring covers most of the common needs
  Built-in scoring has been extensively tested
  Built-in scoring takes BIASING weights automatically into account
  Built-in scoring has refined algorithms for track subdivision
  Built-in scoring comes with utility programs that allow to evaluate statistical errors
Scoring can be geometry dependent AND/OR geometry independent FLUKA can score particle fluences, current, track length, energy spectra, Z spectra, energy deposition...
Either integrated over the “run”, with proper normalization, OR event-by event
Standard scoring can be weighted by means of simple user routines
Notes: <number>

## Slide 4: Related Scoring Commands
USRTRACK, USRCOLL score average d/dE (differential fluence) of a given type or family of particles in a given region
USRBDX scores average d2/dEd (double-differential fluence or current) of a given type or family of particles on a given surface
USRBIN scores the spatial distribution of energy deposited, or total fluence (or star density, or momentum transfer) in a regular mesh (cylindrical or Cartesian) described by the user
USRYIELD scores a double differential yield of particles escaping from a surface. The distribution can be with respect to energy and angle, but also other more “exotic” quantities
SCORE scores energy deposited (or star density) in all regions
The output of SCORE will be printed in the main (standard) output, written on logical output unit LUNOUT (pre-defined as 11 by default)
All other detectors write their results into logical output units assigned by the user (the unit numbers must be >20)
Notes: <number>

## Slide 5: More “Special” Scoring
RESNUCLEi scores residual nuclei in a given region
  more details are given in the respective lecture on activation
DETECT scores energy deposition in coincidence or anti-coincidence with a trigger, separately for each “event" (primary history)
EVENTBIN is like USRBIN, but prints the binning output after each event instead of an average over histories
ROTPRBIN sets the storage precision (single or double) and assigns rotations/translations for a given user-defined binning (USRBIN or EVENTBIN)
  more details will be given in the lecture about the use of LATTICE
TCQUENCH sets scoring time cut-offs and/or Birks quenching parameters for binnings (USRBIN or EVENTBIN) indicated by the user
USERDUMP defines the events to be written onto a “collision tape” file
AUXSCORE defines filters and conversion coefficients
Notes: <number>

## Slide 6: The FLUKA Output Files
The respective Fluka output consists of:
A main (standard) output, written on logical output unit LUNOUT (predefined as 11 by default) [.out]
  for details refer to the lecture explaining the FLUKA output
A file with the last random number seeds, unit LUNRAN (2 by default) [ran*]
A file of error messages, unit LUNERR (15 by default) [.err]
Any number (including zero) of estimator output files. Their logical unit number is defined by the user [*fort_xx*]
The available range of logical output numbers is: 21-99
Generally, the user can choose between formatted and unformatted (binary) scoring (negative or positive sign)
Possible additional output generated by the user in any user routine
Notes: <number>

## Slide 7: Extending ex_4 with Scoring: ex_5.inp
Cylinder along Z, filled by water-aluminum-lead and surrounded by Air
the USRBIN command allows to superimpose to the geometry a 3-D grid, either cartesian or R-Z-Φ
On this grid, one can score energy deposition, particle fluence (total or by particle type), as well as the density of interactions
There is an equivalent EVENTBIN command, that outputs the same quantities event-by-event
using USERWEIG the results can be weighted by the comscw.f or fluscw.f functions
Evolution of ex 4.inp: added new material and scoring
Notes: <number>

## Slide 8: USRBIN
** energy deposition
USRBIN 11.0 ENERGY -40.0 10.0 15.0 TargEne
USRBIN 0.0 -5.0 100.0 200.0 &
This is an R-Z-Φ binning (what(1)=11), scoring energy deposition (generalized particle ENERGY, or 208), writing the unformatted output on unit 40, spanning 0<R<10 in 100 bins, 0<<2 in 1 bin (default), -5<z<15 in 200 bins.
** neutron fluence
* R-Z EM energy output unit Rmax axis Y Zmax
* Rmin axis X Zmin # R-bins # Phi-bins # Z-bins
USRBIN 11.0 NEUTRON -40.0 10.0 15.0 TargNeu
USRBIN 0.0 -5.0 100.0 200.0 &
This is a R-Z-Φ binning (what(1)=11), scoring neutron fluence, writing the unformatted output on unit 40, spanning 0<R<10 in 100 bins, 0<<2 in 1 bin (default), -5<z<15 in 200 bins.
Notes: <number>

## Slide 9: USRBIN  The Result
WHAT(2) = ENERGY :Energy deposition from a 3.5 GeV proton beam hitting at [0.,0.,0.] directed along z results are normalized to GeV/cm3 per primary
Notes: <number>

## Slide 10: USRBIN  The Result
Same, WHAT(2)= NEUTRON to get neutron fluence results are normalized to particles/cm2 per primary
Notes: <number>

## Slide 11: USRBIN  The Result
Same, WHAT(2)= HAD-CHAR to get charged hadron fluence results are normalized to particles/cm2 per primary
Notes: <number>

## Slide 12: USRBDX
USRBDX scores double differential (energy and angle) particle distributions across a boundary surface. The angle is with respect to the normal of the surface. The distribution can be fluence or current, one-way or two-ways, according to WHAT(1):
*out from lead
USRBDX 99.0 HAD-CHAR -50. TARGS3 INAIR 329.87 Sp3ChH
USRBDX 10.0 0.001 40. &
Score charged hadrons at the outer surface of the lead segment ( from TARGS3 to INAIR). WHAT(1)=99 means: fluence, one-way only, log. intervals in energy. From 1 MeV to 10 GeV in 40 intervals, and one angular interval (default). WHAT(6) is a normalization factor: setting it equal to the surface area provides results normalized to cm-2 sr-1. Output to unformatted unit 50
USRBDX 99.0 HAD-CHAR -54. TARGS2 TARGS3 78.5398 Sp2ChHA
USRBDX 10.0 0.001 40. 3.0 &
Score at the surface between 2nd and 3rd target section, same as before but in 3 angular bins.
Notes: <number>

## Slide 13: USRBDX  The Result
Evolution of charged hadron spectra at the various surfaces results are normalized to /GeV/cm2/sr per primary
This is true only if the surface area is explicitly given
Notes: <number>

## Slide 14: USRBDX  The Result
Double differential charged hadron spectra for different angles; results are normalized to /GeV/cm2/sr per primary
Notes: <number>

## Slide 15: USRTRACK
Calculates fluence as a function of energy by scoring track-length in a given volume. Results are normalized to /GeV/cm2/primary
* log neutrons outp. unit region volume # bins
* Emax Emin
USRTRACK -1.0 NEUTRON -55. TARGS3 628.31 40. TrChH
USRTRACK 10.0 0.001 &
remember: USRBDX scores on a surface, while USRBIN scores fluence in volumes and gives no differential information
Notes: <number>

## Slide 16: USRYIELD
Scores a double-differential particle yield around an extended or a point target.
“Energy-like” quantities
“Angle-like” quantities (in degrees or radians)
Notes: <number>

## Slide 17: USRYIELD
While option USRBDX calculates angular distributions WITH RESPECT TO THE NORMAL to the boundary at the point of crossing, USRYIELD's distributions are calculated WITH RESPECT TO THE BEAM DIRECTION (or a different direction specified with SDUM=BEAMDEF).
* 124 = 24 + 1 * 100 => polar angle (in degrees) and kinetic energy
* outp. unit Reg1 Reg2 Norm
* Amax Amin # A bins Emax Emin dbl.differential
USRYIELD 124.0 PIONS+- -57. TARGS3 INAIR 1.0 YieAng
USRYIELD 180.0 0.0 18. 10.0 0.0 3.0 &
Only one interval is possible for the second variable, BUT results are normalized as Double Differential: (in this case, particles/GeV/sr)
Notes: <number>

## Slide 18: USRYIELD -> The Result
pion angular distribution
Notes: <number>

## Slide 19: FILTERS : AUXSCORE
There is the possibility to filter the estimators, restricting the scoring to a selected subset of particles.
For instance: USRBIN energy deposition by muons only
USRBIN 11.0 ENERGY -40.0 10.0 15.0 TargEne
USRBIN 0.0 -5.0 100.0 200.0 &
AUXSCORE USRBIN MUONS TargEne TargEne
Assign the “muons” filter to the USRBIN estimator named TargEne
Another example: score the yield of 56-Iron ions (very useful: there is no separate name for each ion specie, except light ones. HEAVYION score all isotopes heavier than alpha’s together!)
USRYIELD 124.0 ALL-PART -87. TARGS3 INAIR 1.0 Fe56
USRYIELD 180.0 0.0 18. 10.0 0.0 3.0 &
AUXSCORE USRYIELD -5602600. Fe56 Fe56
The requested ion is coded in what(2) according to its A, Z and (optionally) isomeric state m:
what(2) = - (100*Z + 100000*A + m*100000000)
with 0==all , i.e. 2600 == all Iron isotopes
Notes: <number>

## Slide 20: User Conversions/Weighing
Scored fluences are often folded with user-provided response functions to obtain dose equivalent, material activation, etc. This can be done off-line or (at some cost in CPU but with higher accuracy) on line at the time of scoring.
Command USERWEIG:
  with WHAT(3) > 0. makes all fluences and yields scored by USRBIN, USRBDX, USRTRACK , USRYIELD, USRCOLL to be multiplied by a user-written function FLUSCW at scoring time,
  when USRBIN is used to score tracklength
  with WHAT(6) > 0. makes all energy and star densities scored by SCORE, USRBIN to be multiplied by a user-written function COMSCW at scoring time, when USRBIN is used to score dose or stars
For details concerning these conversions please refer to the lecture covering the user routines
Notes: <number>

## Slide 21: Built-in Conversions and AUXSCORE
For some quantities, there is the possibility to get built-in conversions, without the need for user routines: done with generalized particles:
DOSE (obvious..) in GeV/g
SI1MEVNE Silicon 1 MeV-neutron equivalent fluence
HADGT20M Hadrons fluence with energy > 20 MeV
DOSE-EQ Dose Equivalent (pSv)
The set of conversion coefficients used to calculate DOSE-EQ can be selected by the user among a list (see manual) with AUXSCORE:
USRBIN 11.0 DOSE-EQ -40.0 10.0 15.0 TargDEQ
USRBIN 0.0 -5.0 100.0 200.0 &
AUXSCORE USRBIN TargDEQ TargDEQ AMB74
Scores equivalent dose by folding the particle fluences with the “AMB74” conversion coefficients
WARNING : no coefficients available for heavy ions !!!
Notes: <number>

## Slide 22: Standard Postprocessing Programs
To analyze the results of the different scoring options, several programs are available
The most powerful ones are kept in $FLUPRO/flutil.
They assume that the estimator files are unformatted, and can calculate standard deviations and integral values over many cycles:
  ustsuw.f to analyze USRTRACK and USRCOLL outputs
  usxsuw.f to analyze USRBDX outputs
  usysuw.f to analyze USRYIELD outputs
  usbsuw.f to analyze USRBIN outputs
  usrsuw.f to analyze RESNUCLEi outputs
Each of these programs (except usbsuw) produces three files:
  a text file with extension _sum.lis which contains averages, standard deviations, cumulative (integral) quantities
  an unformatted file which can replace the N unformatted estimator files and can be used for further calculations
  a text file with extension _tab.lis to be easily readout by graphic codes
Simpler programs are also provided in the manual, as guides for users
who would like to write their own analysis program.
Notes: <number>

## Slide 23: Standard Postprocessing Programs
Example of tab.lis for usrbdx
# Detector n: 1 Sp2ChH (integrated over solid angle)
# N. of energy intervals 40
1.000E-03 1.259E-03 1.343E-03 4.688E+01
.
..
# double differential distributions
# number of solid angle intervals 3
# 0.000E+00 2.094E+00 2.094E+00 4.189E+00 4.189E+00 6.283E+00
#
1.000E-03 1.259E-03 4.337E-04 5.493E+01 2.077E-04 9.900E+01 0.000E+00 0.000E+00
1.259E-03 1.585E-03 2.360E-04 6.883E+01 0.000E+00 0.000E+00 5.481E-04 9.900E+01
.
.
First comes the angle-integrated quantity then the limits of the angular bins, then the double differential distribution
| In 1st ang. bin | In 2nd ang. bin | In 3rd ang. bin |
Emin Emax | result error | result error | result error |
Notes: <number>

## Slide 24: Flux/Fluence: A Common Confusion
The term Flux is often used, sloppily, to indicate a vaguely defined quantity visualized as “a flow of particles through a surface”.
But Flux is defined by ICRU as dN/dt (particles per unit time). [Where? For which purpose? It looks like a very useless quantity, and is not a “flow”]
What we really need is a quantity that is proportional to effects such as induced activity, dose, radiation damage. These effects are proportional to the number of interactions in a given volume: a “flow of particles” is not what we need!
The number of interactions in a volume is equal to the number of mean free paths travelled by the particles in that volume: therefore it is proportional to the total particle path length. The quantity
is called Fluence
although its “official” definition is with N being the number of particle crossing an element of surface dα PERPENDICULAR to the particle direction. This definition is equivalent but hides its actual physical meaning.
Notes: <number>

## Slide 25: Flux/Fluence: A Common Confusion
Fluence is a point quantity, a function of position (like temperature)
But we are generally interested on
  its average over a volume (total track length density divided by the volume: USRTRACK, USRBIN)
  its average over a surface (USRBDX)
How can a track length be calculated on a surface? Imagine the surface to have an infinitesimal thickness dt : a particle incident with an angle θ with respect to the normal to the surface will travel a segment dt/cos θ. Therefore, we can calculate an average surface fluence by adding dt/cos θ for each particle crossing the surface, and dividing by the volume S dt (S being the area of the surface)
Fluence is DIFFERENT from CURRENT across a given surface: I=dN/da
 is independent from S, I is NOT!
The interaction rate on a given surface is proportional to , not to I
NOTE: If the path-length is measured in units of mean free paths , this expression leads naturally to the density of collisions 
Notes: <number>

## Slide 26: Formal Equivalence of Fluence Definitions
If dA is the surface of the ICRU sphere of cross-sectional area da, then of course is dA=4da
It is known that for a convex body the mean chord length is L=4V/A
Therefore, according to the ICRU definition: is the total chord length of the N particles crossing the sphere (Proof from the book of I. Lux and L. Koblinger, p. 24. A different demonstration can be found in A.B. Chilton, Health Phys. 34, 716 (1978) and 36, 638 (1979) )
But although the two definitions are equivalent, that of ICRU hides the fact that Fluence is a measure of the concentration of particle paths in an infinitesimal element of volume around a space point
And the more cm travelled in that volume, the more are the interactions! (Or the potential interactions, if in vacuum)
Notes: <number>